## Slide 1
Overview of the DAB+ System
Dr. Les Sabel - WorldDMB Technical Committee
2013

## Slide 2
DAB Family of Standards
DAB+ Features
Ensemble Structure
System Structure
Network Options
The Future
Overview of the DAB+ System

## Slide 3
An introduction
Welcome to the DAB Family of Standards
One family provides the most cost effective delivery of digital radio and mobile TV

## Slide 4
The DAB Family of Standards
The Eureka Family of Standards
DAB : 1995 Original audio with PAD and data services standard
T-DMB : 2006 Added video services for Mobile TV and enhanced data streaming
DAB+ : 2007 Enhanced audio service efficiency
Why DAB+?
One family provides the most cost effective delivery of digital radio and mobile TV
2.5 times more audio services than DAB due to the use of HE AAC+ v2
Slightly better coverage – 1 to 2dB better than DAB – better FEC coding
More flexibility for Programme Associated Data delivery
PAD content has much stronger error protection

## Slide 5
DAB Standards
For detailed description of the DAB+ system refer to the following ETSI standards documents
EN 300 401 Main document
TR 101 496-1, -2, -3 Guidelines of use and operation
TS 102 563 Transport of AAC audio
See http://www.worlddab.org
or
http://www.etsi.org/standards

## Slide 6
DAB+ Features
Overview of the DAB+ System

## Slide 7
Australian example
Simulcast stations (AM / FM) new DAB+ only stations
DAB+ Features
Audio - Room for Lots of Services

## Slide 8
Choose the station from a list
No more need to remember the station’s frequency!!!
Station list
Easy to choose a station, listener has more information about the services available
DAB+ Features

## Slide 9
Programme Associated Data (PAD)
Dynamic Label Segment – Text Delivery
Straight forward, effective
Up to 128 characters per text segment
All DAB+ receivers have DLS text display
Good receivers block text display or appropriate scrolling speed
DAB+ Features

## Slide 10
Programme Associated Data
Slideshow (SLS) Images
Further strengthens the audio message
Standalone advertising during song items
Promotion of station activities
Traffic and weather reports
Local news, happenings, community events
Sports results and stock market information
DAB+ Features

## Slide 11
Data Services
Electronic Programme Guide (EPG)
Very useful tool for promotion of programs, talent, competitions
Especially useful for multilingual national broadcasters with scheduled programme slots
Is flexible, can be station, network or ensemble based
Some receivers can record programs for later listening
DAB+ Features

## Slide 12
Data Services – Other
Traffic e.g. TMC and TPEG can provide up to the moment information on
current traffic flow and congestion
fuel locations and prices
parking
Journaline
Hierarchical categorised text service
Custom Applications can be developed
DAB+ Features

## Slide 13
Ensemble Structure
Overview of the DAB+ System

## Slide 14
Ensemble Structure
Ensemble Structure
Multiple different radio stations transmitting on the same frequency
Multiple different radio stations use the same transmitter
Multiple different radio stations share the cost of that single transmission
Very flexible to ensure the broadcaster can deliver the content they provide in the most cost effective manner

## Slide 15
Ensemble Structure
An Ensemble will typically carry multiple services from multiple radio networks,
for example:
Network 1 – 2 stations (services) 128kbps
Network 2 – 4 stations 256kbps
Network 3 – 3 stations 192kbps
Network 4 – 9 stations 576kbps
Total 18 stations 1152kbps
Each network can have their own allocated capacity on the ensemble
  No other network has access to that capacity
Each network can reconfigure their allocated capacity anytime without impacting the other networks’ services
  Pop-up services change their name and sometimes bit rate regularly
Ensemble Structure

## Slide 16
Ensemble Structure
Ensemble 1
Network 1 allocation, e.g. 128kbps
Network N allocation, e.g. 192kbps
Sub-Channel 0
Sub-Channel 1
M
M+1
M+2
Total Capacity = 1152kbps (FEC = EEP3A)
Station A
Station B
64kbps
64kbps
32kbps
64kbps
96kbps
Station X
Station Y
Station Z
Ensemble Structure

## Slide 17
Ensemble Structure
Each ensemble has
its own Ensemble Label
its own unique Ensemble ID code
can carry a unique identifying code of the transmitter (TII)
a Signalling Channel – the Fast Information Channel (FIC)
  Provides details about all services (stations) carried
    Service labels
    Bit rates
    Data location in the stream
  Provides details of all data services and PAD
  Provides announcements and warnings
Ensemble Structure

## Slide 18
System Structure
Overview of the DAB+ System

## Slide 19
System Structure
Example DAB+ network
PAD system
Audio Encoders x N
Local Controller
Service Mux
(Opt)
Studio 1
Switch / Router
Broadcast System
Ensemble Controller
EMUX
DMUX
COFDM
Main Transmitter
COFDM
Repeater Transmitter
Telecoms
cloud
Telecoms
cloud
PAD system
Audio Encoders x M
Service Mux
(Opt)
Studio N
Local Controller
IP is generally preferred for both contribution networks
and distribution networks

## Slide 20
DAB+ Audio
HE AAC+ V2 audio encoding table combinations
Coding Technologies / Dolby AAC+ implementation
Many combinations to allow the most cost effective delivery of different audio content types
System Structure

## Slide 21
DAB+ Audio Encoding
Spectral Band Replication
Efficient sample rate and bit rate reduction method
Only slight audio degradation
System Structure

## Slide 22
DAB+ Audio Encoding
Signal Flow with outer layer FEC
Outer layer of FEC coding and interleaving provides protection for PAD – especially important to ensure robust SLS image delivery
System Structure

## Slide 23
Audio - PAD
PAD for DLS and SLS delivery
XPAD size, music/speech flag, command channel
Typical use: SBR on @ 24kHz core sampling rate, 3 frames per super-frame, 1 super-frame per 120mS
System Structure

## Slide 24
Audio Bit Rates v PAD Bit Rate
Need to ensure the correct balance between audio bit rate, audio settings and PAD
Sub-Channel bit rate (kbps) | FEC Overhead 10% | Payload capacity (kbps) | PAD (kbps) | Audio bit rate (kbps)
32 | 3.2 | 28.8 | 1 | 27.8
32 | 3.2 | 28.8 | 2 | 26.8
32 | 3.2 | 28.8 | 4 | 24.8
32 | 3.2 | 28.8 | 8 | 20.8
48 | 4.8 | 43.2 | 1 | 42.2
48 | 4.8 | 43.2 | 2 | 41.2
48 | 4.8 | 43.2 | 4 | 39.2
48 | 4.8 | 43.2 | 8 | 35.2
64 | 6.4 | 57.6 | 1 | 56.6
64 | 6.4 | 57.6 | 2 | 55.6
64 | 6.4 | 57.6 | 4 | 53.6
64 | 6.4 | 57.6 | 8 | 49.6
64 | 6.4 | 57.6 | 16 | 41.6
80 | 8 | 72 | 1 | 71
80 | 8 | 72 | 2 | 70
80 | 8 | 72 | 4 | 68
80 | 8 | 72 | 8 | 64
80 | 8 | 72 | 16 | 56
Audio bit rate ≈ Sub-Channel bit rate *0.9 – PAD bit rate
SLS images are best synchronised with audio using pre-delivered images and header update display triggers, either
TriggerTime = time/date or
TriggerTime = now
System Structure

## Slide 25
Signal Flow - Transmitter
DAB+ Outer layer FEC coding and interleaving here
System Structure

## Slide 26
FEC Code Rate Comparison
FEC Code | Code Rate | Capacity (kbps) | Number of 64kbps channels | Approximate power required relative to 3A
1A | 1/4 | 576 | 9 | -3 to -6dB
2A | 3/8 | 864 | 13 | -2 to -3dB
3A | 1/2 | 1152 | 18 | 0
3B | 2/3 | 1536 | 24 | +3dB
4A | 3/4 | 1728 | 27 | +6dB
Payload capacity and transmit power can be traded
Stronger FEC protection = lower capacity BUT lower power for the same coverage area
System Structure

## Slide 27
Transmission Structure
Signalling and service information is sent in the Fast Information Channel
96mS
System Structure

## Slide 28
DAB+ Transmission – Australian VHF channels
2 DTV channels allocated = 14MHz = 8 DAB channels = 8A, B, C, D, 9A, B, C, D
Initial Band III allocation for metro cities
System Structure

## Slide 29
Overview
RF Spectrum
Signal bandwidth = 1536 carriers at 1kHz each => 1.535MHz
Channel bandwidth = 1.712 MHz
Channel edge shoulders at -40dB
Far off adjacent power at <-60dB
System Structure

## Slide 30
Network Options
Overview of the DAB+ System

## Slide 31
Star Network
Central multiplexing equipment
Privacy
Stations are in control of their content
Individual links per studio site
Simple networking
This architecture is often used for stand-alone / isolated installations such as single city or area transmissions
Network Options

## Slide 32
Star Network
Number of service encoders, PAD and redundancy can vary between broadcasters
Redundant common ensemble multiplexing and transmitters
Network Options

## Slide 33
Mesh Network
Transparent interconnect between sites
Typically uses a multicast enabled VPN
High Redundancy and Reliability
Content produced at any site can be transmitted at any site
Suitable for distributed broadcast networks such as national multi-studio networks
Network Options

## Slide 34
Monitoring Equipment - Overview
ETI Monitor
Service Monitor
In-Field Monitors
Ensemble Recorder
Tx Monitor
Listeners
Network Options
Repeaters
Multiple monitoring points throughout the system allow rapid fault finding and rectification
Listeners provide the ultimate feedback!!

## Slide 35
Network Management System
Network Management is essential for rapid fault detection and correction
Virtually all equipment now has SNMP fault reporting
Remote access via web interface allows best grade of service
Network Options

## Slide 36
Examples of DAB+ multiplexer and transmitter equipment
Network Options

## Slide 37
The Future
Overview of the DAB+ System

## Slide 38
The Future – Hybrid Radio
DL+ and CAT-SLS are examples of Hybrid Radio
Providing More Information to listeners on demand
Tagging and reminders for later content use
The standards are being written now!
Hybrid Radio combines digital radio broadcast to deliver audio and common PAD to many AND the internet to provide individual actions and services
Hybrid Radio

## Slide 39
What is Hybrid Radio
Free to Air DAB+ broadcast with PAD
Telco network
Broadcaster interaction
3rd Party services
Transmission Information from Broadcaster
Broadcaster
WiFi connection
Hybrid Radio
Touchscreen for basic actions
Bluetooth connection
for browser actions
Home Operation

## Slide 40
What is Hybrid Radio
Mobile Operation
Free to Air DAB+ broadcast with PAD
DAB+ capable mobile phone can use full range of hybrid functions
Mobile network
3rd party services
Mobile internet
Broadcaster interaction
Broadcaster
Transmission Information from Broadcaster

## Slide 41
More Information: Use Case Example 1 – connection to an advertiser
Hybrid Radio Use Cases
Screen tap
Accessing a website from a URL delivered associated with a product / service being advertised

## Slide 42
More Information: Use Case Example 2 – Artist Information
Listeners can access more information about the current artist, tour dates, biographical info, purchase
Screen tap
Hybrid Radio Use Cases

## Slide 43
More Information: Use Case Example 3 – Public Information
Accessing a website from a URL delivered associated with the information provided
Button press
Hybrid Radio Use Cases

## Slide 44
More Information: Use Case Example 4 – Sports Results
Drives listeners to use additional broadcaster facilities, value add advertising and cross promotion
What sport is on tonight, current and previous results, betting
Screen tap
Hybrid Radio Use Cases

## Slide 45
Summary – Top Tips
Overview of the DAB+ System
DAB+ is the best Digital Radio delivery system available
Proven technology
Cost effective infrastructure
Deployed worldwide and expanding rapidly
Very flexible operation for broadcasters
Huge range of receiver products
Great features including scrolling text, images, EPG and data services
Many new developments including Interactivity

## Slide 46
For more information
les.sabel@scommtech.com.au